## Slide 1: Sun Based Localization

## Slide 2: Premise
The algorithms being used will assume that the object to be localized is in a GPS denied environment with no prior knowledge of location.
We want to find a general location based on calculable information relating to the position of the sun and current UTC time.

## Slide 3: Assumed Variables and Conditions
We have a camera that can track onto the sun or we have the ability to gather object height and shadow lengths
We have the ability to know true north
We have the current time and date in Coordinated Universal Time (UTC)

## Slide 4: What Needs to be Calculated Pre Search
The Solar Azimuth – This is the angle of the sun relative to North (Degrees)
Solar Altitude/Elevation – This is the angle of the sun over the horizon (Degrees)
Lat, Lon – Current Lat, Lon can be estimated using the calculated azimuth and elevation.

## Slide 5: Pre Search Calculations
Solar Azimuth and Elevation with Camera
Assuming the camera at our disposal is on a gimble, we can take that data to extract our angles.
We will also need to account for the angle of the vehicle.
- IMU
- Horizon detection and leveling

## Slide 6: Pre Search Calculations Continued
Solar Azimuth with Shadow
If all we have is a shadow and object we can still find what we need.
The solar azimuth can be calculated by measuring the angle clockwise from north that a shadow takes from a top down view of the casting object.

## Slide 7: Pre Search Calculations Continued
Solar Elevation with Shadow
If all we have is a shadow and object we can still find what we need.
The solar elevation can be found using the tangent between the height of an object and its corresponding shadow

## Slide 8: Starting the Search
Once a local azimuth and altitude have been found, we can use that along with our UTC time to begin testing for our current latitude and longitude

## Slide 9: How we are Finding Lat Lon
To find our Lat Lon, we are going to use an iterative refinement search.
Iterative Refinement – We will begin by taking large steps across the globe to find generalizations and then stepping down our search size as we get closer
***Note, we could cut down the testing size simply by eliminating certain lat lons based on day or night

## Slide 10: Calculating Solar Position Based On Lat and Lon
To Calculate the solar position we will need
- Latitude and Longitude (Iterative)
- Current Date and UTC Time at Location
- Elapsed Julian Days (calculated by subtracting current date from January 1st, 2000)
- Declination Angle
- Hour Angle

## Slide 11: Testing
For Testing we used a manually imported expected azimuth and elevation.
In the future we hope to integrate this for use with camera calculations as previously discussed.
Tested on different global cities at there local noon in UTC time.
Ran each city 1800 times stepping 0.1 degrees between -3 and 3 for each alt and az.

## Slide 12: Small Scale Testing With Intentional Error
NOAA data was used for small scale tests
The website provided azimuths and altitudes for specific locations and times
Allowed for testing on several cities around the the world

## Slide 13: Example Result
Targeting Bismark, ND

## Slide 14: Testing more locations
Once single run tests were working we than ran a large scale test on randomly generated Cities.
- We randomly generated over 9,000 (9,334 to be exact) random combinations of cities and times to be ran
- Each city followed the same parameters as the individual tests

## Slide 15
Large Scale Testing Results

## Slide 16
Large Scale Testing Results (Zoomed)
Notes: Means percentile below 300: 96.69988213864781%
Medians percentile below 300: 97.78206364513018%
Minimums percentile below 300: 98.74638379942141%
Maximums percentile below 300: 81.58148505303761%

## Slide 17: Appendix
- Supporting Math
- Single Test Images
- Large Test Result graphs

## Slide 18: Calculating Solar Declination Angle
The angular distance from the zenith of the observer at the equator and the sun at solar noon
dOmega = 2.1429 - 0.0010394594 * dElapsedJulianDays
dMeanLongitude = 4.8950630 + 0.017202791698 * dElapsedJulianDays # Radians
dMeanAnomaly = (6.2400600 + 0.0172019699 * dElapsedJulianDays)
dEclipticLongitude = dMeanLongitude + 0.03341607 * math.sin(dMeanAnomaly) + 0.00034894 * math.sin(2 * dMeanAnomaly) - 0.0001134 - 0.0000203 * math.sin(dOmega)
dEclipticObliquity = 0.4090928 - 6.2140e-9 * dElapsedJulianDays + 0.0000396 * math.cos(dOmega)
dSin_EclipticLongitude = math.sin(dEclipticLongitude)
dY = math.cos(dEclipticObliquity) * dSin_EclipticLongitude
dX = math.cos(dEclipticLongitude)
dRightAscension = math.atan2(dY, dX) if dRightAscension < 0.0: dRightAscension += (2 * math.pi)
dDeclination = math.asin(math.sin(dEclipticObliquity) * dSin_EclipticLongitude)

## Slide 19: Calculating Solar Hour Angle
The angular displacement of the sun east or west of the local meridian due to rotation of the earth on its axis at 15° per hour with morning being negative and afternoon being positive
# Local Standad Time Meridian
LSTM = 15 * abs(0) # LSTM = 15 * UTC Difference which is zero if given UTC Time
# Equation of time
B = math.radians((360/365) * (day_of_year - 81))
EoT = 9.87*math.sin(2*B) - 7.53*math.cos(B) - 1.5*math.sin(B)
# Time Correction Factor
TC = 4 * (longitude - LSTM) + EoT
# Local Solar Time
LST = ((60 * datetime.hour) + datetime.minute + TC) / 60
# Hour Angle
hour_angle = math.radians(15 * (LST - 12))

## Slide 20: Calculating Solar Alt, and Azm Angles
altitude_angle = math.asin(math.sin(latitude) * math.sin(declination_angle) +
math.cos(latitude) * math.cos(declination_angle) *
math.cos(hour_angle))
azimuth_angle = math.atan2(-math.cos(declination_angle) * math.sin(hour_angle),
math.cos(latitude) * math.sin(declination_angle) -
math.sin(latitude) * math.cos(declination_angle) *
math.cos(hour_angle))
altitude_deg = math.degrees(altitude_angle)
azimuth_deg = math.degrees(azimuth_angle)

## Slide 21: Results 1
Targeting Bismark, ND

## Slide 22: Results 1 Stats
Targeting Bismark, ND

## Slide 23: Results 2
Targeting Honolulu, HI

## Slide 24: Results 1 Stats
Targeting Honolulu, HI

## Slide 25: Results 3
Targeting Johannesberg, South Africa

## Slide 26: Results 1 Stats
Targeting Johannesberg, South Africa

## Slide 27: Results 4
Targeting Lima, Peru

## Slide 28: Results 1 Stats
Targeting Lima, Peru

## Slide 29: Results 5
Targeting London, England

## Slide 30: Results 1 Stats
Targeting London, England